# Product Specifications

| Customer |  |
| --- | --- |
| Model Name | S035Q01 |
| Description | Stand LCD Module 320x3RGBx240 Dots 3.5" TFT LCD |
| Date | 2011/12/07 |
| Revision | 1.2 |

| Customer Approval |
| --- |
| Date |  |
| The above signature represents that the product specifications, testing regulation, and warranty in the specifications are accepted |

Elpa Displays, Inc. - 2300 N. Barrington Road #400 - Hoffman Estates, Il 60169 - Ph: 847-519-7205 - Email: info@elpadisplays.com

| Engineering |
| --- |
| Check | Date | Prepared | Date |

# Table of Contents

Coversheet................................................................................................................................1

Record of Revision....................................................................................................................3

1.    General Specifications ...................................................................................................4

2.    Input/Output Terminals ...................................................................................................5

3    Absolute Maximum Ratings ............................................................................................6

4    Electrical Characteristics................................................................................................. 6

5    Timing Chart....................................................................................................................8

6    Optical Characteristics ..................................................................................................14

7    Environmental / Reliability Tests....................................................................................16

8    Mechanical Drawing......................................................................................................18

9    Packing Drawing ...........................................................................................................19

10    Precautions For Use of LCD modules..........................................................................20

# Record of Revision

| Rev | Issued Date | Description | Editor |
| --- | --- | --- | --- |
| V1.1 | 2011/04/16 | First Release. | Richard Liang |
| V1.2 | 2011/12/07 | Add SPI Command | Tiger |

1  General Specifications

| Feature | Spec |
| --- | --- |
| Characteristics | Size | 3.5inch |
|  | Resolution | 320(RGB) X 240 |
|  | Interface | RGB |
|  | Color Depth | 24bit |
|  | Technology type | a-Si |
|  | Display Spec. Pixel pitch (mm) | 0.219 x 0.219 |
|  | Display colors | 16.7M Dithering |
|  | Pixel Configuration | R.G.B. Vertical Stripe |
|  | Display Mode | Normally White |
|  | Surface Treatment | HC |
|  | Gray Scale Inversion Direction | 12 CLOCK |
| Mechanical | LCM (W x H x D) (mm) | 76.9*64.0*3.05 |
|  | Active Area(mm) | 70.08 x 52.56 |
|  | With /Without TSP | Without TSP |
|  | Weight (g) | TBD |
|  | LED Numbers | 6 LEDs |

Note 1: Viewing direction for best image quality is different from TFT definition, there is a 180 degree shift.

Note 2: Requirements on Environmental Protection: RoHS

Note 3: LCM weight tolerance: +/- 5%

2  Input/Output Terminals

Pin assignment

| Pin No. | Symbol | Description |
| --- | --- | --- |
| 1,2 | VBL- | Backlight LED Cathode |
| 3,4 | VBL+ | Backlight LED Anode. |
| 5~7 | NC | NC |
| 8 | RESET | Reset Signal pin (“Low” is enable) |
| 9 | CS | Chip select |
| 10 | SCL | Serial Clock. |
| 11 | SDI | Serial Data |
| 12-19 | B0~B7 | Data bus |
| 20-27 | G0~G7 | Data bus |
| 28-35 | R0~R7 | Data bus |
| 36 | HSYNC | Line Synchronous Signal |
| 37 | VSYNC | Frame Synchronous Signal |
| 38 | DOTCLK | Dot-clock signal and oscillator source |
| 39-40 | NC | NC |
| 41-42 | VCC | Power supply for logic operation |
| 43-47 | NC | NC |
| 48 | NC | NC |
| 49 | NC | NC |
| 50 | NC | NC |
| 51 | NC | NC |
| 52 | DEN | Display enable signal |
| 53-54 | GND | System Ground |

- Absolute Maximum Ratings

- Driving TFT LCD Panel

| Item | Symbol | MIN | MAX | Unit | Remark |
| --- | --- | --- | --- | --- | --- |
| Supply Voltage | VDD | -0.3 | 5.0 | V |  |
| Operating Temperature | TOPR | -20 | 70 | ℃ |  |
| Storage Temperature | TSTG | -30 | 80 | ℃ |  |

- Electrical Characteristics

  - Driving TFT LCD Panel

| Item | Symbol | MIN | TYP | MAX | Unit | Remark |
| --- | --- | --- | --- | --- | --- | --- |
| Supply Voltage | VDD | 3.0 | 3.3 | 3.6 | V |  |
| Input Signal Voltage | Low Level | VIL | GND | - | 0.1x VDD | V |  |
|  | High Level | VIH | 0.8x VDD | - | VDD | V |  |
| TFT Common Electrode | VcomH | 2.5 | - | 4.5 | V |  |
| Voltage | VcomL | -3 | - | 0 | V |  |
| TFT Gata ON Voltage | VcomH |  |  | 15 | V |  |
| TFT Gata OFF Voltage | VcomL | -10 |  |  | V |  |

4.2  Driving Backlight

| Parameter | Symbol | Conditions | Min. | Typ. | Max. | Unit |
| --- | --- | --- | --- | --- | --- | --- |
| Supply voltage of white LED backlight | VLED =V(BL+)- V(BL-) | Forward current =20mA Number of LED dies = 6 |  | 19.8V |  | V |

# Note : The figure below shows the connection of backlight LED.

4.3  Block Diagram

# 5  Timing Chart

# 5.1 AC Electrical Characteristics

# 5.2  24 Bit RGB Mode (@ SEL\[3:0] = 1100 or 1101)

# 5.3  Timing Diagram

# 5.4  Vertical Timing Diagram (HV Mode)

# 5.5  Vertical Timing Diagram (DE Mode)

# 5.6  Input Data Timing (24 bit RGB mode for 960 x 240 @ SEL\[3:0] = 1100b)

# 5.7  3-Wire Serial Port Interface (Default Register Map)

void SPIByteWrite(unsigned char reg, unsigned char data)

{

int i;

int j;

unsigned short value=0;

value= (reg & 0x3f) << 10;

value |= (0x0200 | data);

for(i=0;i<16;i++)

{

LCDCSLow();

LCDClockLow();

msWait(25);

j=value& 0x8000;

if(j==0x8000)

{

LCDDataHigh();

}

else

{

LCDDataLow();

}

msWait(25);

LCDClockHigh();

msWait(25);

value<<=1;

}

LCDCSHigh();

msWait(200);

}

//*******************Send SPI Command*************************//

SPIByteWrite(0x01,0x00);

SPIByteWrite(0x02,0x03);//HDNC[1:0]  //0x03

SPIByteWrite(0x03,0xcc);//c4 or c5

SPIByteWrite(0x04,0x46);

SPIByteWrite(0x05,0x0d);

SPIByteWrite(0x06,0x00);

SPIByteWrite(0x07,0x00);

SPIByteWrite(0x08,0x08);

SPIByteWrite(0x09,0x40);

SPIByteWrite(0x0a,0x88);

SPIByteWrite(0x0b,0x88);

SPIByteWrite(0x0c,0x20);

SPIByteWrite(0x0d,0x20);

SPIByteWrite(0x0e,0x67);  //0x62

SPIByteWrite(0x0f,0xA4);

SPIByteWrite(0x10,0x04);

SPIByteWrite(0x11,0x24);

SPIByteWrite(0x12,0x24);

SPIByteWrite(0x1E,0x00);

SPIByteWrite(0x20,0x00);  // WNSEL1[1:0]

6  Optical Characteristics

# Optical specifications

| Items | Symbol | Condition | Specifications | Unit | Note |
| --- | --- | --- | --- | --- | --- |
|  |  |  | Min. | Typ. | Max. |  |  |
| Contrast Ratio | CR |  | - | 350 | - | - |  |
| Response Time | TR |  | - | 25 | 40 | ms |  |
|  | TF |  | - | 25 | 40 | ms |  |
| Chromaticity | Red | XR |  | 0.586 | 0.636 | 0.686 | - |  |
|  |  | YR |  | 0.300 | 0.350 | 0.400 | - |  |
|  | Green | XG |  | 0.261 | 0.311 | 0.361 | - |  |
|  |  | YG |  | 0.501 | 0.551 | 0.601 | - |  |
|  | Blue | XB |  | 0.084 | 0.134 | 0.184 | - |  |
|  |  | YB |  | 0.101 | 0.151 | 0.201 | - |  |
|  | White | XW |  | 0.261 | 0.311 | 0.361 | - |  |
|  |  | YW |  | 0.300 | 0.353 | 0.400 | - |  |
| Viewing angle | Hor. | 1(3 o’clock) | Center CR≥10 | 50 | 60 | - | deg. |  |
|  |  | 2(9 o’clock) |  | 50 | 60 | - |  |  |
|  | Ver. | 2(12 o’clock) |  | 30 | 40 | - |  |  |
|  |  | 1(6 o’clock) |  | 50 | 60 | - |  |  |
| NTSC ratio |  |  |  |  | 50 |  | % |  |
| Luminance |  | L |  | 250 | 300 |  |  |  |

Note 1: Definition of Contrast Ratio (CR):

The contrast ratio can be calculated by the following expression.

Contrast Ratio (CR) = L63 / L0

L63: Luminance of gray level 63

L0: Luminance of gray level 0

CR = CR (10)

CR (X) is corresponding to the Contrast Ratio of the point X at Figure in Note 5.

# Note 2: Definition of Response Time (TR, TF):

# Note 3: Viewing Angle

The above “Viewing Angle” is the measuring position with Largest Contrast Ratio; not for good image quality. View Direction for good image quality is 6 O’clock. Module maker can increase the “Viewing Angle” by applying Wide View Film.

# Note 4: Measurement Set-Up:

The LCD module should be stabilized at a given temperature for 20 minutes to avoid abrupttem perature change during measuring. In order to stabilize the luminance, the measurement

should be executed after lighting Backlight for 20 minutes in a windless room.

7  Environmental / Reliability Tests

8  Mechanical Drawing

9  Packing

Packing Method

1. Put module into tray cavity:

2. Tray stacking

3. Put 1 cardboard under the tray stack and 1 cardboard above:

4. Fix the cardboard to the tray stack with adhesive tape:

5. Put the tray stack into carton.

6. Carton sealing with adhesive tape.

10  Precautions For Use of LCD modules

# 10.1  Handling Precautions

10.1.1. The display panel is made of glass. Do not subject it to a mechanical shock by dropping it from a high place, etc.

10.1.2. If the display panel is damaged and the liquid crystal substance inside it leaks out, be sure  not to get any in your mouth, if the substance comes into contact with your skin or clothes, promptly wash it off using soap and water.

10.1.3. Do not apply excessive force to the display surface or the adjoining areas since this may cause the color tone to vary.

10.1.4. The polarizer covering the display surface of the LCD module is soft and easily scratched. Handle this polarizer carefully.

10.1.5. If the display surface is contaminated, breathe on the surface and gently wipe it with a soft dry cloth. If still not completely clear, moisten cloth with one of the following solvents:

－  Isopropyl alcohol

－  Ethyl alcohol

Solvents other than those mentioned above may damage the polarizer. Especially, do not use the following:

－  Water

－  Ketone

－  Aromatic solvents

10.1.6. Do not attempt to disassemble the LCD Module.

10.1.7. If the logic circuit power is off, do not apply the input signals.

10.1.8. To prevent destruction of the elements by static electricity, be careful to maintain an optimum work environment.

# 10.1.8.1. Be sure to ground the body when handling the LCD Modules.

10.1.8.2. Tools required for assembly, such as soldering irons, must be properly ground.

# 10.1.8.3. To reduce the amount of static electricity generated, do not conduct assembly and other work under dry conditions.

10.1.8.4. The LCD Module is coated with a film to protect the display surface. Be care when peeling off this protective film since static electricity may be generated.

10.2  Storage Precautions

10.2.1. When storing the LCD modules, avoid exposure to direct sunlight or to the light of fluorescent lamps.

10.2.2. The LCD modules should be stored under the storage temperature range If the LCD modules will be stored    for a long time, the recommend condition is:

Temperature : 0℃ ～  40℃    Relatively humidity: ≤80%

10.2.3.   The LCD modules should be stored in the room without acid, alkali and harmful gas.

# 10.3  Transportation Precautions

The LCD modules should be no falling and violent shocking during transportation, and also should avoid excessive press, water, damp and sunshine.